## Slide 1: CG3207 – Lab 3 Demo
Group 17
Ishaan Singal – A0078549L
Karthik Rajasekaran – A0091523L
Raunak Rajpuria – A0074900L

## Slide 2: Overview
All operations required in Lab 3b have been implemented
Integrated with UART wrapper for demo purposes
Implemented pipelining to augment the single cycle design
Using ‘stall’ signal for division operation
Make use of NOPs to avoid hazards

## Slide 3: Demo 1 - LW, SW, ADD, SUB, AND, XOR, BGEZAL/BGEZ, JR, J
Accept user inputs from opd1 and opd2
ADD opd1, opd2 values
If opd2 >= 0 (BGEZAL)
  SUB opd1 and opd2
  Return to instruction after BGEZAL using JR
4. Else
  Store AND of add/sub result and opd2
  Store XOR of opd1 and opd2
  Display results using SW
Loop To Beginning using J

## Slide 4: Demo 2 - LUI, ORI, SLT, BEQ, SRL, ADDI, OR, NOR, SLL, SLLV
Load 61 into higher 16 and 2304 into lower 16 bits of register $s0 using LUI and ORI
Accept user inputs from opd1 and opd2
Check if opd1 is less than $s0 using SLT
If SLT result is equal to 1
  Shift Left $s0 by 16 bits using SLL
  Store NOR of shifted value and opd2 – Result1
  Shift Left opd1 by 1 bit using SLLV – Result2
  Display results using SW
  Loop To Beginning using J
4. Else
  Shift Right $s0 by 16 bits using SRL
  Store OR of shifted value and opd2 – Result1
  Add Opd1 with immediate value 100 using ADDI – Result 2
  Display results using SW
  Loop To Beginning using J

## Slide 5: Demo 3 – MULT/MULTU, JAL, JALR, MFHI, MFLO
Accept user inputs from opd1 and opd2
Multiply opd1 and opd2 using MULT
Jump and link using JAL
Store and display higher 16 bits of multiplication results using MFHI
Link and Return to return address using JALR
Store and display lower 16 bits of multiplication results using MFLO
Jump to beginning using JR/J

## Slide 6: Demo 4 – DIV/DIVU
Accept user inputs from opd1 and opd2
Divide opd1 and opd2 using DIV
Store and display quotient using MFHI
Store and display remainder using MFLO
Jump to beginning using J